SERVICE UPDATE

FROM

NEW YORK BUS SALES, LLC

Product Effected – Any with Light Monitor

Complaint: 	Just installed LED tail/stop lights and the lights on the driver’s light monitor do not work-

Cause:	The rear LED lights do not draw the same as normal incandescent bulbs causing monitor to not recognize the current flow.

Correction: 	The monitor must be changed – We recommend that you replace the monitor with part #0070838, this is a Doran monitor which can distinguish between LED and incandescent lights.

This Service Update was provided to you by New York Bus Sales, LLC.

NYBS is ordering option 30195-12 when a Light Monitor is spec’d which will option this particular monitor

If you find things that might help others in the industry please call or e-mail us:

CHITTENANGO – phone the Service Department at 800-962-5768 or

Daryl Wallace :  dwallace@newyorkbussales.com

Brian Lamaitis :  blamaitis@newyorkbussales.com

ROCHESTER – phone the Service Department at 800-463-3232 or

Dan Quibell :  dpquibell@newyorkbussales.com

Gary Chichester:  gchichester@newyorkbussales.com

ALBANY – phone the Service Department at 866-867-1100 or

Steve Searles: ssearles@newyorkbussales.com