SERVICE UPDATE

FROM

NEW YORK BUS SALES, LLC

***********************

Complaint: 	LED lights on stop arms seem comparatively dimmer than the old incandescent lights-WE HAVE ONLY SEEN THIS ON MICROBIRD UNITS, BUT THERE IS THE POSSIBILITY ON OTHER UNITS

Cause:	Due to the warning lights drawing so much power and the relative lack of draw from the LED lights they do not get a full 12V to power them to full capacity

Correction: 	Using the attached schematic and instructions, install 2 relays into the system to power the stop arm lights.

This Complaint/Correction was provided by OUR OWN Brian Lamaitis

THANK YOU BRIAN!!

If you find things that might help others in the industry please call or e-mail us:

CHITTENANGO – phone the Service Department at 800-962-5768 or

Daryl Wallace @ dwallace@newyorkbussales.com

Brian Lamaitis @ blamaitis@newyorkbussales.com

ROCHESTER – phone the Service Department at 800-463-3232 or

Dan Quibell @ dpquibell@newyorkbussales.com

Gary Chichester @ gchichester@newyorkbussales.com

ALBANY – phone the Service Department at 866-867-1100 or

Steve Searles @ ssearles@newyorkbussales.com