SERVICE NOTICE

IT HAS BEEN BROUGHT TO OUR ATTENTION THAT THERE HAVE BEEN SOME ISSUES SURROUNDING THE BODY SOLENOIDS NOT WORKING PROPERLY WHICH CAUSE SOME ERRATIC EVENTS WITH RESPECT TO THE BODY ELECTRICAL OPERATION

BLUE BIRD IS CURRENTLY WORKING WITH WHITE/ROGERS TO ADDRESS THE ISSUE AND IT IS BELIEVED THAT THERE WAS A “BATCH” OF THESE SOLENOIDS WHICH ARE CAUSING THE ISSUES

IF YOU HAVE UNITS EXPERIENCING THIS ISSUE AT SUB-ZERO TEMPERATURES PLEASE BE ADVISED THAT YOU CAN TAP ON THE SOLENOID AND IT WILL OPERATE PROPERLY

WE ARE REPLACING THESE (#0932012) UNDER WARRANTY AND THEY ARE AS YOU CAN IMAGINE CURRENTLY ON BACKORDER YOU CAN USE (#4286431) IN ITS PLACE WITH A MINOR REWIRE (TAKING THE GROUND –WHITE WIRE – {+} WIRE WITH DIODE AND PUTTING TO THE MOUNTING BOLT)

CHITTENANGO      800-962-5768

HENRIETTA         800-463-3232

ALBANY             866-867-1100

THANK YOU

NEW YORK BUS SALES, LLC.