## Slide 1: Service Update #23-0421
MAKE SURE TO CHECK VALVE STEM CLEARANCE WHEN CHANGING TIRES ON UNITS WITH AIR DISC BRAKES
Just recently, Horseheads Central School had a unit with Air Disc brakes which had an inner dual go flat.
Upon inspection, they found that the valve stem was positioned in such a way that the valve rubbed against a tab on the brake caliper (FIGURE #1) causing a hole in the stem of the valve.
Valve Stems come in a variety of sizes and shapes as shown above and if when mounting a new tire or changing a valve stem for any reason, care should be taken to replace with a “like” stem.
Once mounted, the tires should be rotated to ensure 1/2” of clearance between the valve stem and any obstructions such as the brake caliper.
Tire Valve Stem Clearance with Air Disc Brakes

## Slide 2
PLEASE NOTE:
It is believed that there should have been a “clicking” noise heard when rotating the tire. But due in this case to a brass stem being used, the brass is so soft that there was no noise produced.
Please also alert tire dealers to the possibility of this issue!
FIGURE #1

## Slide 3
Comments or Concerns:
John Johnston
jjohnston@newyorkbussales.com
Cell 315-263-0766
Director of Service
Ryan Hemund
rhemund@newyorkbussales.com
Chittenango: 800-962-5768
Daryl Wallace
dwallace@newyorkbussales.com
Brian Lamaitis
blamaitis@newyorkbussales.com
Bob Reith
breith@newyorkbussales.com
Phil Tucker
ptucker@newyorkbussales.com
Albany: 866-867-1100
Ben Reiling
breiling@newyorkbussales.com
Rochester: 800-463-3232
Brandon Shepard
bshepard@newyorkbussales.com
Middletown: 845-609-7070
Moncia Mc Donald
mmcdonald@newyorkbussales.com
CONTACT ANY OF OUR SERVICE LOCATIONS WITH QUESTIONS
Notes: Set up as a table would make it easier to edit
Add additional pages