## Slide 1: Service Update #23-0117
New “Style” Diode
Recently we had a newer BBCV (Vision) Diesel unit with NEA (New Electrical Architecture) experiencing an intermittent engine code related to the Aftertreatment system. While diagnosing the issue we found that a new style “Busman Diode” (FIGURE #1) is being used on the circuit board in the PDU.
We found that there were 4 diodes in the circuit board, shown on diagram inside the PDU cover and in the circuit board in FIGURES #2, #3 & #4. We then started with the diodes and testing them which all appeared and tested fine. While looking into the issue we went to start the unit and found that it would not crank! Seeing as the diodes were the only items which were touched, we started to look into which diode was in the circuit and found location D1 was where the diode was located. We checked to ensure that the arrow was pointing down for correct polarity (FIGURE #5) and removed the diode again for inspection.
We found that the cover could be removed exposing the diode (FIGURE #6), and when we did, we found that the diode is supposed to clip into a small metal bracket (FIGURE#7) and this one did not which was causing the intermittent issues we were seeing!
Busman Diode Issue

## Slide 2
FIGURE #1
FIGURE #2
FIGURE #3

## Slide 3
FIGURE #4
FIGURE #5

## Slide 4
FIGURE #7
FIGURE #6
BLUE BIRD PART #10017834

## Slide 5
Comments or Concerns:
John Johnston
jjohnston@newyorkbussales.com
Cell 315-263-0766
Director of Service
Ryan Hemund
rhemund@newyorkbussales.com
Chittenango: 800-962-5768
Daryl Wallace
dwallace@newyorkbussales.com
Brian Lamaitis
blamaitis@newyorkbussales.com
Bob Reith
breith@newyorkbussales.com
Phil Tucker
ptucker@newyorkbussales.com
Albany: 866-867-1100
Ben Reiling
breiling@newyorkbussales.com
Rochester: 800-463-3232
Brandon Shepard
bshepard@newyorkbussales.com
Middletown: 845-609-7070
Moncia Mc Donald
mmcdonald@newyorkbussales.com
CONTACT ANY OF OUR SERVICE LOCATIONS WITH QUESTIONS
Notes: Set up as a table would make it easier to edit
Add additional pages